## Slide 1: Chapter 3 Logic Gates
逻辑门

## Slide 2: The Inverter 反相器 (也称非门)
The inverter performs the Boolean NOT operation, the Boolean expression for an inverter is
  or x=A’
Truth table
Input | Output
A | X
0 | 1
1 | 0

## Slide 3: The Inverter 反相器 (也称非门)
The negation and polarity indicators.
否定和极性指示
Active high
Active low
Active high
Active low

## Slide 4: The inverter
Example waveforms:
A
X
A group of inverters can be used to form the 1’s complement of a binary number:
Binary number
1 0 0 0 1 1 0 1
0 1 1 1 0 0 1 0

## Slide 5: The AND Gate 与门
An AND gate produces a HIGH output only when all of the inputs are HIGH.
The AND operation:
  X = A·B X = AB
  X=A*B X=A∧B
Truth table
Input |  | Output
A | B | X
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 6: The AND Gate
Tow or more inputs.
One single output.

## Slide 7: The AND Gate
Example waveforms:
A
X
B
An AND gate produces a HIGH output only when all of the inputs are HIGH.

## Slide 8: The AND Gate
The AND operation is used in computer programming as a selective mask. If you want to retain certain bits of a binary number but reset the other bits to 0, you could set a mask with 1’s in the position of the retained bits.
Example: If the binary number 10100011 is ANDed with the mask 00001111, what is the result?
00000011

## Slide 9: The OR Gate 或门
The OR gate produces a HIGH output if any input is HIGH.
The OR operation:
  X=A+B X=A∨B
Truth table
Input |  | Output
A | B | X
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 10: The OR Gate 或门
Tow or more inputs.
One single output.

## Slide 11: The OR Gate
Example waveforms:
A
X
B
The OR gate produces a HIGH output if any input is HIGH; if all inputs are LOW, the output is LOW.

## Slide 12: The OR Gate
The OR operation can be used in computer programming to set certain bits of a binary number to 1.
Example: ASCII letters have a 1 in the bit 5 position for lower case letters and a 0 in this position for capitals. (Bit positions are numbered from right to left starting with 0.) What will be the result if you OR an ASCII letter with the 8-bit mask 00100000?
The resulting letter will be lower case (e.g. a=0x61 A=0x41).

## Slide 13: The NAND Gate 与非门
The NAND (NOT AND) operation:
The NAND gate produces a LOW output when all inputs are HIGH; otherwise, the output is HIGH.
Truth table
Input |  | Output
A | B | X
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 14: The NAND Gate 与非门
Tow or more inputs.
One single output.

## Slide 15: The NAND Gate
Example waveforms:
A
X
B
The NAND gate produces a LOW output when all inputs are HIGH; otherwise, the output is HIGH.

## Slide 16: The NAND Gate
The NAND gate is particularly useful because it is a “universal” gate – all other basic gates can be constructed from NAND gates.
Question: How would you connect a 2-input NAND gate to form a basic inverter?

## Slide 17: The NOR Gate 或非门
The NOR (NOT OR) operation:
Truth table
Input |  | Output
A | B | X
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Tow or more inputs.
One single output.

## Slide 18: The NOR Gate
Example waveforms:
A
X
B
The NOR gate produces a LOW output if any input is HIGH; if all inputs are HIGH, the output is LOW.

## Slide 19: The NOR Gate
Example: When is the LED is ON for the circuit shown?
The LED will be on when any of the four inputs are HIGH.

## Slide 21: The XOR Gate 异或门(EX-OR)
The XOR (exclusive or ) operation:
Truth table
Input |  | Output
A | B | X
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 22: The XOR Gate
Example waveforms:
A
X
B
Notice that the XOR gate will produce a HIGH only when exactly one input is HIGH.
Question: If the A and B waveforms are both inverted for the above waveforms, how is the output affected?
There is no change in the output.

## Slide 23: The XnOR Gate 同或门(EX-NOR)
The XNOR (exclusive not or ) operation:
  or
Truth table
Input |  | Output
A | B | X
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 24: The XNOR Gate
Example waveforms:
A
X
B
Notice that the XNOR gate will produce a HIGH when both inputs are the same. This makes it useful for comparison functions.
Question: If the A waveform is inverted but B remains the same, how is the output affected?
The output will be inverted.

## Slide 25: IEEE Logic Symbols
Function
表示功能的名字或符号
Output variables
输出变量
Input variables
输入变量

## Slide 26: IEEE Logic Symbols
X
Y
Z
&
Z=XY
X
Y
Z
+
Z=X+Y
X
Y
Z
>=1
X
X
X
X

## Slide 27: IEEE Logic Symbols
X
Y
Z
=1
X
Y
Z
=1
X
Y
Z
+
X
Y
Z
&

## Slide 28: Fixed Function Logic* 固定功能逻辑
Two major fixed function logic families are TTL （双极型）and CMOS（互补金属氧化物半导体）. A third technology is BiCMOS（双CMOS）, which combines the first two. Packaging for fixed function logic is shown.
DIP package
双引线封装
SOIC package
小轮廓集成电路封装

## Slide 29: Fixed Function Logic*
00: 4 NAND gates
02: 4 NOR gates
04: 16 INVERTERs
……

## Slide 30: Fixed Function Logic*
Logic symbols show the gates and associated pin numbers

## Slide 31: Fixed Function Logic*
Data sheets include limits and conditions set by the manufacturer .

## Slide 32: Fixed Function Logic*
SN74ALS00
生产者
德州仪器公司
54--- 军用温度范围(-55℃~125℃)
74--- 商用温度范围(0℃ ~70℃)
  低功耗（L）
  高速（H）
  低功耗肖特基 (LS)
  肖特基 (S)
  先进低功耗肖特基 (ALS)
  先进肖特基 (AS)
商用先进低功耗肖特基“与非”门集成电路

## Slide 33: Handling Precautions for CMOS* (Page 85)
CMOS逻辑芯片对静电非常敏感，如果操作不当，CMOS会由于静电放电（ESD）而损坏，如下为注意事项：
  保存和安放在导电泡沫上
  把仪器和地连接上
  手腕串联一个大电阻和地连接
  在电源没有关上时，不要把芯片拔掉
  电源关上时，不要加信号电压