## Slide 1: CHAPTER 6 FUNCTIONS OF COMBINATIONAL LOGIC
组合逻辑电路函数

## Slide 2: Encoders 编码器
An encoder is a digital circuit that performs the inverse operation of a decoder. An encoder has 2n input lines and n output lines.
The output lines generate the binary equivalent of the input line whose value is 1.

## Slide 3: Encoders
E.g. 8-to-3 binary encoder (octal-to-binary)
A0=D1+D3+D5+D7
A1=D2+D3+D6+D7
A2=D4+D5+D6+D7

## Slide 4: Encoders
One signal at a time.

## Slide 5: Priority Encoders 优先编码器
Multiple asserted inputs are allowed; one has priority over all others.
E.g. 4-to-2 Priority Encoder Truth Table
Inputs |  |  |  | Outputs |  | 
D3 | D2 | D1 | D0 | A1 | A0 | V
0 | 0 | 0 | 0 | X | X | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | X | 0 | 1 | 1
0 | 1 | X | X | 1 | 0 | 1
1 | X | X | X | 1 | 1 | 1

## Slide 6: 8-to-3 Priority Encoder

## Slide 7: Priority EncoderS

## Slide 8: Encoders
The decimal to BCD is an encoder with an input for each of the ten decimal digits and four outputs that represent the BCD code for the active digit.
There is no zero input because the outputs are all LOW when the input is zero.
E.g. Show how the decimal-to-BCD encoder converts the decimal number 3 into a BCD 0011
1
0
0
1
1

## Slide 9: Encoders
The 74HC147 is an example of an IC encoder. It is has ten active-LOW inputs and converts the active input to an active-LOW BCD output.
Decimal input
BCD output
GND
VCC
HPRI/BCD
74HC147
This device is offers additional flexibility in that it is a priority encoder(优先编码器). This means that if more than one input is active, the one with the highest order decimal digit will be active.

## Slide 10: Encoders
Keyboard encoder

## Slide 11: Code converters 代码转换器
There are various code converters that change one code to another. Two examples are the four bit binary-to-Gray converter and the Gray-to-binary converter.
E.g. Show the conversion of binary 0111 to Gray and back.
0
0
0
1
1
1
Binary-to-Gray Gray-to-Binary
MSB
LSB
MSB
LSB
1
0
0
0
1
0
0
1
1
1

## Slide 12: Multiplexers 数字多路器
“Selects” binary information from one of many input lines and directs it to a single output line. Also know as the “selector” circuit.
Selection is controlled by a particular set of inputs lines whose output depends on the combination of the data input lines.
For a 2n-to-1 multiplexer, there are 2n data input lines and n selection lines whose bit combination determines which input is selected

## Slide 13: Multiplexers

## Slide 14: 4-1 Multiplexer 4-1多路器
S1 | S0 | Y
0 | 0 | D0
0 | 1 | D1
1 | 0 | D2
1 | 1 | D3
Y = S1’S0’D0 + S1’S0D1 + S1S0’D2 + S1S0D3=∑miDi

## Slide 15: 4-1 Multiplexer
Two select lines are shown here to choose any of the four data inputs.
Question
Which data line is selected if S1S0 = 10?
Data
select
Data
inputs
Data
output
D1
D0
D2
D3
S1
S0
D2
1
0

## Slide 16: 8-to-1 MUX
Y = C’B’A’D0 + C’B’AD1
+ C’BA’D2 + C’BAD3
+ CB’A’D4 + CB’AD5
+ CBA’D6 + CBAD7
=∑miDi
If G’=1 then Y=0, W=1

## Slide 17: 8-to-1 MUX

## Slide 18: Multiplexer Expansions 多路器扩展
Until now, we have examined single-bit data selected by a MUX. What if we want to select m-bit data/words?
Combine MUX blocks in parallel with common select and enable signals
Example: Construct a logic circuit that selects between 2 sets of 4-bit inputs (see next slide for solution).

## Slide 19: Example: Quad 2-to-1 MUX
Uses four 2-to-1 MUXs with common select (S) and enable (E).
Select line chooses between Ai’s and Bi’s. The selected four-wire digital signal is sent to the Yi’s
Enable line turns MUX on and off (E=1 is on).

## Slide 20: Example: Quad 4-to-1 MUX

## Slide 21: Multiplexer Expansions
A 16-1 multiplexer using two 74LS151

## Slide 22: Multiplexer Expansions
A 32-to-1 multiplexer using four 8-to-1 multiplexers and a 2-to-4 decoder

## Slide 23: Implementing Boolean functions with Multiplexers
E.g. Using an 8-to-1 multiplexer to realize the Boolean function F=f(x,y,z)=∑(1,2,4,5,7)
Y=C’B’A’D0 + C’B’AD1 + C’BA’D2 + C’BAD3 + CB’A’D4 + CB’AD5 + CBA’D6 + CBAD7
F=f(x,y,z) = ∑(1,2,4,5,7) =x’y’z+x’yz’+xy’z’+xy’z+xyz
C=x,B=y,A=z
D0=D3=D6=0 D1= D2= D4= D5= D7=1

## Slide 24: Implementing Boolean functions with Multiplexers
C=x,B=y,A=z D0=D3=D6=0 D1= D2= D4= D5= D7=1

## Slide 25: Implementing Boolean functions with Multiplexers
Using an 4-to-1 multiplexer to realize the Boolean function F=f(x,y,z)=∑(1,2,4,5,7)
F = f(x,y,z) = ∑(1,2,4,5,7) =x’y’z+x’yz’+xy’z’+xy’z+xyz
Let B=x, A=y
1
1
1
1
xy
z
10
11
01
00
1
0
1
F
x
y
z
z’
1
z
D0=z, D1=z’
D2=1, D3=z
F = x’y’D0+x’yD1+xy’D2+xyD3

## Slide 26: Implementing Boolean functions with Multiplexers
Using an 4-to-1 multiplexer to realize the Boolean function F=f(x,y,z)=∑(1,2,4,5,7)
F = f(x,y,z) = ∑(1,2,4,5,7) =x’y’z+x’yz’+xy’z’+xy’z+xyz
Let B=x, A=y
F
x
y
z
z’
1
z
D0=z, D1=z’
D2=1, D3=z
F = x’y’D0+x’yD1+xy’D2+xyD3
x | Y | Z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Y = S1’S0’D0 + S1’S0D1 + S1S0’D2 + S1S0D3=∑miDi
D0=z

## Slide 27: Implementing Boolean functions with Multiplexers
Using an 4-to-1 multiplexer to realize the Boolean function F=f(x,y,z)=∑(1,2,4,5,7)
F = f(x,y,z) = ∑(1,2,4,5,7) =x’y’z+x’yz’+xy’z’+xy’z+xyz
Let B=x, A=y
F
x
y
z
z’
1
z
D0=z, D1=z’ D2=1, D3=z
F = x’y’D0+x’yD1+xy’D2+xyD3

## Slide 28: Implementing Boolean functions with Multiplexers
Using an 4-to-1 multiplexer to realize the Boolean function F=f(x,y,z)=∑(1,2,4,5,7)
F = f(x,y,z) = ∑(1,2,4,5,7) =x’y’z+x’yz’+xy’z’+xy’z+xyz
Let B=x, A=z
1
1
1
1
xy
z
10
11
01
00
1
0
1
F
x
z
y
y’
y’
1
D0=y, D1=y’
D2=y’, D3=1
F = x’z’D0+x’zD1+xz’D2+xzD3

## Slide 29: Implementing Boolean functions with Multiplexers
Using an 4-to-1 multiplexer to realize the Boolean function F=f(x,y,z)=∑(1,2,4,5,7)
F = f(x,y,z) = ∑(1,2,4,5,7) =x’y’z+x’yz’+xy’z’+xy’z+xyz
Let B=z, A=y
1
1
1
1
xy
z
10
11
01
00
1
0
1
F
z
y
x
x’
1
x
D0=x, D1=x’
D2=1, D3=x
F = z’y’D0+z’yD1+zy’D2+zyD3

## Slide 30: exercise
Implement function using a 4-to-1 MUX
F(X,Y,Z) = Σm(1,2,6,7)
F(A,B,C) = Σm(1,3,5,6)

## Slide 31: exercise
F(X,Y,Z) = Σm(1,2,6,7) = X’Y’Z + X’YZ’ + XYZ’ + XYZ
There are n=3 inputs. The first n-1 (=2) inputs serve as the selection lines
1
1
1
XY
Z
10
11
01
00
1
0
1
F
x
y
z
z’
0
1

## Slide 32: exercise
F(X,Y,Z) = Σm(1,2,6,7) = X’Y’Z + X’YZ’ + XYZ’ + XYZ

## Slide 33: exercise
F(A,B,C) = ∑m(1,3,5,6)
A | B | C |  | F
0 | 0 | 0 |  | 0
0 | 0 | 1 |  | 1
0 | 1 | 0 |  | 0
0 | 1 | 1 |  | 1
1 | 0 | 0 |  | 0
1 | 0 | 1 |  | 1
1 | 1 | 0 |  | 1
1 | 1 | 1 |  | 0
A=B=0
F=C
A=0 B=1
F=C
A=1 B=0
F=C
A=B=1
F=C’
1
1
AB
C
10
11
01
00
1
0
1
1
F
C
C
C’
C
A
B

## Slide 34: Implementing Boolean functions with Multiplexers
E.g. Consider the following Boolean expression given in sum-of-product form:
F(x1,x2,x3)=x1’x2’+x1x2’+x1x3
Derive a circuit for using only 2-to-1 multiplexers.

## Slide 35: Implementing Boolean functions with Multiplexers
D0=X2’
D1=X2’+X3
1
1
1
1
x1x2
x3
10
11
01
00
1
0
1

## Slide 36: exercise
F(A,B,C,D)=∑m(1,2,4,9,10,11,12,14,15)
Derive a circuit for using 4-to-1 multiplexers.
(Do it yourself)

## Slide 37: MUX as a Universal Gate
We can construct OR, AND, and NOT gates using 2-to-1 MUXs. Thus, 2-to-1 MUX is a universal gate.
z = x0 + x0’x1
= x1 + x0
z = x·0 + x’·1
= x’
z = x0x1 + x0’·0
= x0x1

## Slide 38: HOMEWORK
F(A,B,C,D)=∑m(0,3,4,5,7,9,13,15)
Derive a circuit for using 8-to-1 multiplexers.

## Slide 39: Demultiplexers 多路分配器
A demultiplexer (DEMUX) performs the opposite function from a MUX. It switches data from one input line to two or more data lines depending on the select inputs.

## Slide 40: Demultiplexers
The 74LS138（3-8译码器） was introduced previously as a decoder but can also serve as a DEMUX.
When connected as a DEMUX, data is applied to one of the enable inputs, and routed to the selected output line depending on the select variables.
74LS138
Data select lines
Enable
inputs
Data outputs

## Slide 41: Parity Generators/Checkers 奇偶发生器/校验器
Parity is an error detection method that uses an extra bit appended to a group of bits to force them to be either odd or even. In even parity, the total number of ones is even; in odd parity the total number of ones is odd.
E.g. The ASCII letter S is 1010011. Show the parity bit for the letter S with odd and even parity.
  odd parity: 11010011
  even parity: 01010011

## Slide 42: Parity Generators/Checkers
The 74LS280 can be used to generate a parity bit or to check an incoming data stream for even or odd parity.
Checker: The 74LS280 can test codes with up to 9 bits. The even output will normally be HIGH if the data lines have even parity; otherwise it will be LOW. Likewise, the odd output will normally be HIGH if the data lines have odd parity; otherwise it will be LOW.

## Slide 43: Parity Generators/Checkers
Generator:
To generate even parity, the parity bit is taken from the odd parity output.
To generate odd parity, the output is taken from the even parity output.