## Slide 1: Chapter 8 shift registers
移位寄存器

## Slide 2: Registers 寄存器
A n-bit register is a set of n flip-flops that is capable of storing n bits of binary information.
With added combinational gates, the register can perform data-processing tasks.
Some basic data movements are show on the next page.

## Slide 4: Shift Register
A register capable of shifting its stored bits laterally in one or both directions is called a shift register.
The logical configuration of a shift register consists of a chain of flip-flops in cascade, with the output of one flip-flop connected to the input of the next FF.

## Slide 5: Serial-in/Serial out Shift Register 串行输入/串行输出移位寄存器
The figure shows a 4-bit device implemented with D flip-flops.

## Slide 6: Serial-in/Serial out Shift Register
E.g. four bits(1101) is entered serially into the register.
0 | 0 | 0 | 0
0 | 0 | 0 | 1
MSB
LSB
1101
Clock 1
0 | 0 | 1 | 1
101:0
Clock 2
0 | 1 | 1 | 0
01:00
Clock 3
1 | 1 | 0 | 1
1:000
Clock 4
How to get the data out of the register?
The bits must be shifted out serially and taken off the Q3

## Slide 7: Serial-in/Serial out Shift Register 串行输入/串行输出移位寄存器
The figure shows a 4-bit device implemented with D flip-flops.

## Slide 8: Serial-in/Serial out Shift Register
E.g. four bits(1101) is entered serially into the register.
0 | 0 | 0 | 0
1 | 0 | 0 | 0
MSB
LSB
1101
Clock 1
0 | 1 | 0 | 0
0:110
Clock 2
1 | 0 | 1 | 0
00:11
Clock 3
1 | 1 | 0 | 1
000:1
Clock 4

## Slide 9: serial in/parallel out shift register 串入并出寄存器
parallel out

## Slide 10: Parallel in/Serial out Shift Register 并入串出寄存器
Shift registers can be used to convert parallel data to serial form. A logic diagram for this type of register is shown:
Explain the function of the input.

## Slide 11: Parallel in/parallel out
4-bit register
6-bit register

## Slide 12: Registers with parallel load
Next page shows a 4-bit register with a control input Load that is directed through gates into the D inputs of the flip-flops.
When Load is 1, the data on the four inputs is transferred into the register with the next positive transition of a clock pulse.
When Load is 0, the data inputs are blocked, and the D inputs of the flip-flops are connected to their outputs.

## Slide 14: Shift register with parallel load
Shift | Load | Operation
0 | 0 | Nothing
0 | 1 | Load parallel
1 | X | Shift

## Slide 15: Bidirectional Shift Register
Bidirectional shift registers can shift the data in either direction with the control input.

## Slide 16: Universal Shift Register 通用移位寄存器
S1S0 | Action
00 | Nothing
01 | Shift down
10 | Shift up
11 | Parallel load
(SN74XX194)

## Slide 17: Shift Register Counters
Shift registers can form useful counters with the output of the last flip-flop fed to the input of the first, making a "circular" or "ring" structure.
Two important shift register counters are the Johnson counter and the ring counter.

## Slide 18: Johnson counter
The Johnson counter can be made with a series of D flip-flops or with a series of J-K flip flops.

## Slide 19: Johnson counter
The Johnson counter is useful when you need a sequence that changes by only one bit at a time but it has a limited number of states (2n, where n = number of flip-flops).
The table shown here is for a 4-bit Johnson counter initialized with all 0.
Johnson counter |  |  |  | 
State | Q0 | Q1 | Q2 | Q3
0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0
2 | 1 | 1 | 0 | 0
3 | 1 | 1 | 1 | 0
4 | 1 | 1 | 1 | 1
5 | 0 | 1 | 1 | 1
6 | 0 | 0 | 1 | 1
7 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0

## Slide 20: Johnson counter
“twist”
Redrawing the same Johnson counter (without the clock shown) illustrates why it is sometimes called as a “twisted-ring” counter(also called switch-tail ring counter, walking ring counter,).

## Slide 21: Ring counter 循环计数器，或环形计数器
A 4-bit ring counter constructed from a series of D flip-flops.

## Slide 22: Ring counter
It must be preloaded with the desired pattern (usually a single 0 or 1) and it has even fewer states than a Johnson counter (n, where n = number of flip-flops.
The table shown here is for a 4-bit ring counter initialized with a single 1.
Straight ring counter |  |  |  | 
State | Q0 | Q1 | Q2 | Q3
0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
2 | 0 | 0 | 1 | 0
3 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
2 | 0 | 0 | 1 | 0
3 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 0

## Slide 23: Ring counter
E.g. An 8-bit ring counter with a preload mode.
The preload mode is repeated every 8 clocks.
需要片数不同，表示状态不同