## Slide 1: Sequential Circuits’ analysis

## Slide 2: Synchronous Sequential Circuit Analysis
Analysis Pinciples
  1. Determine the system variables: input, state, and output.
  2. Determine the flip-flop type. Write the characteristic equations.
  3. write the excitation equations.
  4. write the next state equations.
  5. Write the output variable equations.
Notes: 1.确定系统变量：输入变量、状态变量以及输出变量；
2.确定触发器类型，写出特征方程；
3.写出激励方程；
4.写出次态方程；
5.写出输出方程；
6.构造转换表；
7.为每个状态分配相应符号，构造状态图或状态表；
8.画出时序图（波形图）；
9.功能分析。

## Slide 3: Synchronous Sequential Circuit Analysis
(cont.)
  6. Construct a transition table.
  7. Assign symbols to the states and construct a table or state diagram.
  8. When possible, construct a timing diagram.
  9. Functionality analysis
Notes: 1.确定系统变量：输入变量、状态变量以及输出变量；
2.确定触发器类型，写出特征方程；
3.写出激励方程；
4.写出次态方程；
5.写出输出方程；
6.构造转换表；
7.为每个状态分配相应符号，构造状态图或状态表；
8.画出时序图（波形图）；
9.功能分析。

## Slide 4: Example 1
Analysis the following synchronous sequential circuit, suppose the present state is 00, the input sequence is 0000011111, give the timing diagram.
Notes: 1.输入x
2.输出z
3.两个JK触发器负边沿触发

## Slide 5: Example 1
1. Determine the system variables: input, state, and output.
  input=x
  output=Z
  state variables=y1 and y0
2. Determine the flip-flop type. Write the characteristic equations.
yn+1=Jyn’+k’yn
Notes: 1.确定系统变量：输入变量、状态变量以及输出变量；
  输入变量：x
  输出变量：z
  状态变量：y1、y0
2.确定触发器类型，写出特征方程；
  yn+1=Jyn’+K’yn

## Slide 6: Example 1
3. write the excitation equations.
  K0=J0=1
  K1=J1=x⊕y0
4. write the next state equations.
  y1n+1=J1y1’+k’y1 y0n+1=J0y0’+k0’y0
  y1n+1=x’y1’y0 +x’y1y0’+xy1’y0’+xy1y0 y0n+1=y0’
Notes: 3.写出激励方程；
4.写出次态方程

## Slide 7: Example 1
5. Write the output variable equations
  Z=(xy1’)’=x’+y1
  6. Construct a transition table.
Notes: 5.写出输出方程；
6.构造转换表

## Slide 8: Example 1
  y1n+1= x’y1’y0 +x’y1y0’ +xy1’y0’+xy1y0
  y0n+1=y0’
  Z=(xy1’)’=x’+y1
Y1n+1 K-Map
Z K-Map
Y0n+1 K-Map

## Slide 9: Example 1
7. Assign symbols to the states and construct a table or state diagram
Q1 | 00
Q2 | 01
Q3 | 10
Q4 | 11

## Slide 10: Example 1
8. construct a timing diagram
  y1n+1= x’y1’y0 +x’y1y0’ +xy1’y0’+xy1y0
  y0n+1=y0’
  Z=(xy1’)’=x’+y1

## Slide 11: Example 2
Analysis the following circuit
Notes: 4个输出Q1~Q4
4个D触发器正脉冲触发

## Slide 12: Example 2
1. Determine the system variables: input, state, and output
  state variables: Q1,Q2,Q3, and Q4
  2. Determine the flip-flop type. Write the characteristic equations.
    Qn+1=D
  3. excitation equations
    D4=Q3 D3=Q2 D2=Q1
    D1=Q4’(Q3Q1’)’=Q4’Q3’+Q4’Q1

## Slide 13: Example 2
4. the next state equations
  Q4n+1=Q3
  Q3n+1=Q2
  Q2n+1=Q1
  Q1n+1=Q4’Q3’+Q4’Q1

## Slide 14: Example 2
5. Construct a transition table

## Slide 15: Example 2
6. Assign symbols to the states and construct a table or state diagram

## Slide 16: Example 2
7. construct a timing diagram
CP
Q1
Q2
Q3
Q4
S0 S1 S3 S7 S15 S14 S12 S8 S0

## Slide 17: Exercise
Find the transition table and the state table for the Mealy sequential circuit below.

## Slide 18: Exercise
1. Determine the system variables: input, state, and output
  input: x1,x2
  output: Z
  state variable: Da , Db ,Dc
  2. Determine the flip-flop type. Write the characteristic equations.
    Qn+1=D

## Slide 19: Exercise
3. Excitation equations and output equations
  Da=Qa⊕X2
  Db=Qb⊕X1
  Dc=X1X2Qc’Qa
  Z=X1X2Qc’Qa
4. write the next state equations
  Qan+1=QaX2’+Qa’X2 Qbn+1=QbX1’+Qb’X1 Qcn+1=X1X2Qc’Qa

## Slide 20: Exercise
5. Construct a transition table

## Slide 21: Exercise
6. Assign symbols to the states and construct a state table

## Slide 22: Counters

## Slide 23: Cascaded counters 级联计数器
Cascading is a method of achieving higher-modulus counters.
For synchronous IC counters, the next counter is enabled only when the terminal count of the previous stage is reached.

## Slide 24: Up/Down Synchronous Counters
The 74HC190 is a high speed CMOS synchronous up/down decade counter with parallel load capability. It also has a active LOW ripple clock output () and a MAX/MIN output when the terminal count is reached.
The count enable input.
The ripple clock output.

## Slide 25: Cascaded counters
A modulus-100 counter using two cascaded decade counters
  The terminal count(TC) is analogous to ripple clock output(RCO) on some IC counters.
If fin =100 kHz, what is fout?
fout ：100 kHz/100=1kHz
Notes: 当第10个脉冲(CLK10)到来时，芯片1的TC为高，第二片芯片的CTEN处于有效使能状态，计数一次
当第20个脉冲(CLK20)到来时，芯片1的TC为高，第二片芯片的CTEN处于有效使能状态，计数一次。
……
当第100个脉冲(CLK100)到来时，芯片1的TC为高，第二片芯片的CTEN处于有效使能状态，计数一次，此时芯片2的TC为高。
所以，总的模为10*10=100

## Slide 26: Cascaded counters
Notes: 图1，频率依次/10
图2：频率依次/8，/12，/16，output结果为f/1536
图3：频率依次/10，/4，/7，/5，output结果为f/1400

## Slide 27: Counter Decoding 计数器译码
Decoding is the detection of a binary number and can be done with an AND gate.
What number is decoded by the and gate?

## Slide 28: Partial Decoding 部分译码
The decade counter shown previously incorporates partial decoding (looking at only the MSB and the LSB) to detect 1001. This was possible because this is the first occurrence of this combination in the sequence
Detects 1001 by looking only at two bits

## Slide 29: Resetting the Count with a Decoder
The divide-by-60 counter in the text also uses partial decoding to clear the tens count when a 6 was detected.
Notes: The divide characteristic illustrated here is a good way to obtain a lower frequency using a counter. For example, the 60 Hz power line can be converted to 1 Hz.

## Slide 30: Counter Decoding
E.g. Show how to decode state 5 with an active LOW output.

## Slide 31: A Counter Application: Digital Clock 数字时钟

## Slide 32: Control Signal Generation by Decoding Counter Outputs
E.g. Using counter to realize following control signals
74LS393:
Dual 4-bit Binary Counter.
双四位二进制计数器

## Slide 33: Control Signal Generation by Decoding Counter Outputs
E1 = f(Q3,Q2,Q1,Q0) = m(2,3,8,9,10,11)
E2 = f(Q3,Q2,Q1,Q0) = m(5)
E3 = f(Q3,Q2,Q1,Q0) = m(9)

## Slide 34: Control Signal Generation by Decoding Counter Outputs